## Slide 1
Embedded | Team 2

## Slide 2
Team Leader:
  Abdalla Hammos.
Team Members:
  Mazin Nasr.
  Ahmed Marwan.
  Ali Osama.
  Ahmed Khaled.

## Slide 3
Power Control

## Slide 4
Agenda:
Main Function of the project.
Gained Value.
Project in details.
    Components & Used Technologies.
    Hardware Design.
    Software Design.
Further Updates.

## Slide 5
Main Function of the project:
It allows the user to control loads and devices at his/her home using Smart Phone through WiFi.
Gained Value:
  More easy way to control devices.
  Save time.
  Save power consumption.

## Slide 6
Project in details:
Components & Technologies used:
  C programming language.
  Proteus.
  Microcontroller (ATMega328P).
  Relays.
  ULN2003A.
  LEDS.
  Capacitors.
  Diodes.
  Zener Diodes.
  Resistors.
  Pin Headers & Terminal Blocks.

## Slide 7
Hardware Design:
Switching Circuit for 4 Home Loads

## Slide 8
- The Pin Header at the beginning of the circuit represents the output of
microcontroller which is high or low.
- The ULN2003A IC (Arrray of transistors) receives the signal from microcontroller then it determines if the relay is on when output is 1 or off when output is 0.

## Slide 9
- The LEDs are to indicate if there is a signal from the microcontroller.
- The Switches are to allow manual control of the device when any problems like mobile or Wi Fi not working are present.
- Resistors in parallel with the load to sample some voltage from it.

## Slide 10
- The Diode is for half wave rectification.
- Capacitors are for smoothing the sample rectified voltage.
- Finally Zener Diodes are to make the voltage constant to return it back to microcontroller through another pin header to know if device is on or off.

## Slide 11
Software Design :
Block Diagram
GPIO
Relay
Switching
Relay
Microcontroller
Button
Button

## Slide 12
Layered Diagram
Switching | App Layer
Relay | HWAL
GPIO | MCAL
Button

## Slide 13
According to the Layered Architecture :
1-Microcontroller Abstraction Layer (MCAL):
-GPIO.h file is created to define the main GPIO functions (setting-resetting-reading).
2- Hardware Abstraction Layer (HWAL) :
-Relay.h file is to create all relays in the system.
-Button.h file is to create all inputs in the system (instead of WiFi signal because it isn’t available in current time ).

## Slide 14
3-Application architecture layer :
Switching.h file is to initializing both relays and buttons then controlling relays through varies function.

## Slide 15
Further Updates:
There are various updates could be included:
  Adding measurement technique by including measurement circuit and writing a suitable code.
  We can use some sensors in different applications (ex: temperature sensor in turning air condensing on or off automatically, …. etc).

## Slide 16
Thank You